## Slide 1: IEEE 802.1X Port-Based NAC
Network Security

## Slide 2: IEEE 802.1X Port-Based NAC
Objectives of the Topic
After completing this topic, a student will be able to
  explain basics of IEEE 802.1X access control.

## Slide 3: IEEE 802.1X Port-Based NAC
Figures and material in this topic have been adapted from
“Network Security Essentials: Applications and Standards”, 2014 by William Stallings.

## Slide 4: IEEE 802.1X Port-Based NAC
IEEE 802.1X Port-Based Network Access Control was designed to provide access control functions for LANs.

## Slide 5: IEEE 802.1X Port-Based NAC
Terminology Related to IEEE 802.1X

## Slide 6: IEEE 802.1X Port-Based NAC
Terminology Related to IEEE 802.1X

## Slide 7: IEEE 802.1X Port-Based NAC
Terminology Related to IEEE 802.1X

## Slide 8: IEEE 802.1X Port-Based NAC
The terms supplicant, network access point, and authentication server correspond to the EAP terms peer, authenticator, and authentication server, respectively.

## Slide 9: IEEE 802.1X Port-Based NAC
Until the AS authenticates a supplicant (using an authentication protocol), the authenticator only passes control and authentication messages between the supplicant and the AS.

## Slide 10: IEEE 802.1X Port-Based NAC
The 802.1X control channel is unblocked, but the 802.11 data channel is blocked.

## Slide 11: IEEE 802.1X Port-Based NAC
Once a supplicant is authenticated and keys are provided, the authenticator can forward data from the supplicant, subject to predefined access control limitations for supplicant to network.
Now data channel is unblocked.

## Slide 12: IEEE 802.1X Port-Based NAC
802.1X uses the concepts of controlled and uncontrolled ports.
Ports are logical entities defined within the authenticator and refer to physical network connections.

## Slide 13: IEEE 802.1X Port-Based NAC
Each logical port is mapped to one of these two types of physical ports.

## Slide 14: IEEE 802.1X Port-Based NAC
An uncontrolled port allows the exchange of protocol data units (PDUs) between the supplicant and the AS, regardless of the authentication state of the supplicant.

## Slide 15: IEEE 802.1X Port-Based NAC
A controlled port allows the exchange of PDUs between a supplicant and other systems on the network only if the current state of the supplicant authorizes such an exchange.

## Slide 16: IEEE 802.1X Port-Based NAC
802.1X Access Control